## Slide 1
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Chapter 4 Network Layer:
The Data Plane

## Slide 2
4.1 Overview of Network layer
  data plane 数据平面
  control plane 控制平面
4.2 What’s inside a router路由器
4.3 IP: Internet Protocol
  datagram format
  fragmentation（分片）
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward （通用转发） and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 3: Chapter 4: network layer
chapter goals:
understand principles behind network layer services, focusing on data plane:
  network layer service models
  forwarding versus routing
  how a router works
  generalized forwarding
instantiation, implementation in the Internet

## Slide 4: Network layer
transport segment（报文段） from sending to receiving host
on sending side encapsulates segments into datagrams（数据报）
on receiving side, delivers segments to transport layer
network layer protocols in every host, router
router examines header fields in all IP datagrams passing through it
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical

## Slide 5: Two key network-layer functions
network-layer functions:
forwarding: 转发 move packets from router’s input to appropriate router output
routing: 路由 determine route taken by packets from source to destination
  routing algorithms
analogy: taking a trip
forwarding: process of getting through single interchange
routing: process of planning trip from source to destination

## Slide 6: Network layer: data plane, control plane
Data plane
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
forwarding function
Control plane
network-wide logic 全网络
determines how datagram is routed among routers along end-end path from source host to destination host
two control-plane approaches:
  traditional routing algorithms: implemented in routers
  software-defined networking (SDN): implemented in (remote) servers
1
2
3
0111
values in arriving
packet header

## Slide 7
Per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact in the control plane
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 8
data
plane
control
plane
Logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs)
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header

## Slide 9: Network service model
Q: What service model for “channel” transporting datagrams from sender to receiver?
example services for individual datagrams:
guaranteed delivery
guaranteed delivery with less than 40 msec delay
example services for a flow of datagrams:
in-order datagram delivery
guaranteed minimum bandwidth to flow
restrictions on changes in inter-packet spacing

## Slide 10: Network layer service models:
Network
Architecture
Internet
ATM
ATM
ATM
ATM
Service
Model
best effort
CBR
VBR
ABR
UBR
Bandwidth
none
constant
rate
guaranteed
rate
guaranteed
minimum
none
Loss
no
yes
yes
no
no
Order
no
yes
yes
yes
yes
Timing
no
yes
yes
no
no
Congestion
feedback
no (inferred
via loss)
no
congestion
no
congestion
yes
no
Guarantees ?
未定比特速率（UBR：Unspecified Bit Rate）：对传输速率没有指定，但可靠性要求很高，即所谓"尽力传输"（Best Effort），用于局域网仿真（LAN Emulation）。
不变比特速率（CBR：Constant Bit Rate）：有固定的带宽（速率）要求，适用实时的话音和视频信号传输。
可用比特速率（ABR：Available Bit Rate）：只需指定峰值（Peak）和谷值（Minimum）信元速率，应用不多。
可变比特速率（VBR：Variable Bit Rate）：允许随时可变的带宽，但必须指定峰值带宽、最大突发数据长度和必须维持的最低速率。
ATM是Asynchronous Transfer Mode（ATM）异步传输模式的缩写
Notes: ATM是Asynchronous Transfer Mode（ATM）异步传输模式的缩写

## Slide 11
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 12: Router architecture overview
high-speed
switching
fabric 高速交换结构
routing
processor
router input ports
router output ports
forwarding data plane (hardware) operttes in nanosecond timeframe
routing, management
control plane (software)
operates in millisecond
time frame
high-level view of generic router architecture:
路由选择处理器

## Slide 13: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric
交换结构

## Slide 14: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
using header field values, lookup output port using forwarding table in input port memory (“match plus action”)
destination-based forwarding: forward based only on destination IP address (traditional)
generalized forwarding: forward based on any set of header field values
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric
交换结构

## Slide 15: Destination-based forwarding
Destination Address Range
11001000 00010111 00010000 00000000
through
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through
11001000 00010111 00011111 11111111
otherwise
Link Interface
0
1
2
3
Q: but what happens if ranges don’t divide up so nicely?
forwarding table

## Slide 16: Longest prefix matching
Destination Address Range
11001000 00010111 00010*** *********
11001000 00010111 00011000 *********
11001000 00010111 00011*** *********
otherwise
DA: 11001000 00010111 00011000 10101010
examples:
DA: 11001000 00010111 00010110 10100001
which interface?
which interface?
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix matching
Link interface
0
1
2
3

## Slide 17: Longest prefix matching
we’ll see why longest prefix matching is used shortly, when we study addressing
longest prefix matching: often performed using ternary content addressable memories (TCAMs，三态内容可寻址存储器)
  content addressable: present address to TCAM: retrieve address in one clock cycle, regardless of table size
  Cisco Catalyst: can up ~1M routing table entries in TCAM

## Slide 18: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar
交叉式

## Slide 19: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 20: Switching via a bus（总线）
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 21: Switching via interconnection network（互联网络，纵横式交换结构）
overcome bus bandwidth limitations
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar

## Slide 22: Input port queuing
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking 队头阻塞: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric
Notes: 队头阻塞（HOL Blocking）：
若输入队列头部的包因输出端口冲突被阻塞，后续包即使目标端口空闲也无法转发（即使它们的目标端口不同），导致吞吐量下降（理论最大吞吐约58%）。

## Slide 23: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing
This slide in HUGELY important!
Datagram (packets) can be lost due to congestion, lack of buffers
Priority scheduling – who gets best performance, network neutrality

## Slide 24: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets more
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 25: How much buffering?
RFC 3439 rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
recent recommendation: with N flows, buffering equal to
RTT C
.
N
N： TCP流的数目
C：链路的容量
Notes: N TCP流的数目
链路的容量

## Slide 26: Scheduling mechanisms
scheduling: choose next packet to send on link
FIFO (first in first out) scheduling: send in order of arrival to queue
  real-world example?
  discard policy: if packet arrives to full queue: who to discard?
    tail drop: drop arriving packet
    priority: drop/remove on priority basis
    random: drop/remove randomly
queue
(waiting area)
packet
arrivals
packet
departures
link
(server)

## Slide 27: Scheduling policies: priority
priority scheduling: send highest priority queued packet
multiple classes, with different priorities
  class may depend on marking or other header info, e.g. IP source/dest, port numbers, etc.
  real world example?
high priority queue
(waiting area)
low priority queue
(waiting area)
arrivals
classify
departures
link
(server)
1
3
2
4
5
5
5
2
2
1
1
3
3
4
4
arrivals
departures
packet in service

## Slide 28: Scheduling policies: still more
Round Robin (RR) scheduling:
multiple classes
cyclically scan class queues, sending one complete packet from each class (if available)
real world example?
1
2
3
4
5
5
5
2
3
1
1
3
2
4
4
arrivals
departures
packet in service

## Slide 29: Scheduling policies: still more
Weighted Fair Queuing (WFQ):
generalized Round Robin
each class gets weighted amount of service in each cycle
real-world example?

## Slide 30: 输入端口和输出端口排队对比
Notes: 虚拟输出队列（VOQ）：
在输入端口为每个输出端口维护独立队列，解决HOL阻塞（如Cisco的Crossbar架构）。
组合输入输出排队（CIOQ）：
结合两者优点，输入和输出均设队列，交换结构速率只需稍高于端口速率（如2倍）。
负载均衡架构：
如多级交换（Clos网络）分散拥塞压力。

## Slide 31
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 32: The Internet network layer
forwarding
table
host, router network layer functions:
routing protocols
path selection
RIP, OSPF, BGP
IP protocol
addressing conventions
datagram format
packet handling conventions
ICMP protocol
error reporting
router “signaling”
transport layer: TCP, UDP
link layer
physical layer
network
layer
Notes: RIP（ Routing Information Protocol ）路由信息协议：是在一个AS系统中使用地内部路由选择协议，是基于距离向量路由选择的协议。RIP有两个版本：RIPv1和RIPv2，它们均基于经典的距离向量路由算法，最大跳数为15跳。
RIP的算法简单，但在路径较多时收敛速度慢，广播路由信息时占用的带宽资源较多，它适用于网络拓扑结构相对简单且数据链路故障率极低的小型网络中，在大型网络中，一般不使用RIP。
OSPF（ Open Shortest Path First，开放最短路径优先）协议：采用链路状态路由选择技术，开放最短路径优先算法。路由器互相发送直接相连的链路信息和它拥有的到其它路由器的链路信息。每个 OSPF 路由器维护相同自治系统拓扑结构的数据库。从这个数据库里，构造出最短路径树来计算出路由表。当拓扑结构发生变化时， OSPF 能迅速重新计算出路径，而只产生少量的路由协议流量。
主要优点：
收敛速度快；没有跳数限制；
支持服务类型选路
提供负载均衡和身份认证
BGP （边界网关协议，Border Gateway Protocol ）是自治系统之间的路由选择协议。BGP用于连接Internet。作为最新的外部网关协议，现有四个版本。
BGP 是唯一一个用来处理像因特网大小的网络协议，也是唯一能够妥善处理好不相关路由域间的多路连接协议。BGPv4是一种外部的路由协议。可认为是一种高级的距离向量路由协议。
BGP特点：
BGP是一种外部路由协议，与OSPF、RIP不同，其着眼点不在于发现和计算路由，而在于控制路由的传播和选择最好的路由。
BGP通过携带AS路径信息，可以彻底的解决路由循环问题。
P协议是一种面向无连接的数据报协议，它是一种不可靠的协议，它不提供任何差错检验。因此网际报文控制协议（Internet Control Message Protocol）ICMP出现了，ICMP协议用于IP主机、路由器之间传递控制消息，这里的控制消息可以包括很多种：数据报错误信息、网络状况信息、主机状况信息等，虽然这些控制消息虽然并不传输用户数据，但对于用户数据报的有效递交起着重要作用，从TCP/IP的分层结构看ICMP属于网络层，它配合着IP数据报的提交，提高IP数据报递交的可靠性。ICMP是封装在IP数据报中进行发送的，从这点看来，ICMP协议又有点像一个传输层协议，其实不然，因为ICMP报文的目的不是目的主机上的某个应用程序，它不为应用程序提供传输服务，ICMP报文的目的是目的主机上的网络层处理软件。简单的来说，ICMP协议就像奔波于网络中的一名医生，它能及时检测并汇报网络中可能存在的问题，为解决网络错误或拥塞提供了最有效的手段

## Slide 33: IP datagram format
ver
length
32 bits
data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
32 bit source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
32 bit destination IP address
options (if any)
IP protocol version
number
header length
(bytes)
upper layer protocol
to deliver payload to
total datagram
length (bytes)
“type” of data
for
fragmentation/
reassembly
max number
remaining hops
(decremented at
each router)
e.g. timestamp,
record route
taken, specify
list of routers
to visit.
how much overhead?
20 bytes of TCP
20 bytes of IP
= 40 bytes + app layer overhead

## Slide 34: IP fragmentation, reassembly
network links have MTU (max.transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 35: IP fragmentation, reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
Notes: 分片偏移是要按8 octet来对齐的，也就是按8字节对齐，所以这里的一个单位应该是8字节， 185单位 * 8字节 = 1480字节，也就对的上了。
每个分片的长度都是8字节的整数倍。
这时候就会有偏移量这个东西，偏移量是用来记录每个分片所在的位置，偏移量=相对分片报文长度/8；假设一共传输3800字节，mtu为1400字节，由于固定ip首部为20字节，因此实际传输长度为1420字节，所以只需要传输三次，1400+1400+1000，那么第一片偏移为0，第二片偏移=1400/8=175，第三次偏移=2800/8=350.

## Slide 36
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 37: IP addressing: introduction
IP address: 32-bit identifier for host, router interface
interface(接口): connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
点分十进制记法
Notes: IP地址与接口关联

## Slide 38: IP addressing: introduction
Q: how are interfaces actually connected?
A: we’ll learn about that in chapter 5, 6.
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
A: wired Ethernet interfaces connected by Ethernet switches
A: wireless WiFi interfaces connected by WiFi base station
For now: don’t need to worry about how one interface is connected to another (with no intervening router)

## Slide 39: Subnets（子网）
IP address:
  subnet part - high order bits
  host part - low order bits
what’s a subnet ?
  device interfaces with same subnet part of IP address
  can physically reach each other without intervening router
network consisting of 3 subnets
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 40: Subnets
recipe
to determine the subnets, detach each interface from its host or router, creating islands of isolated networks
each isolated network is called a subnet
subnet mask: /24
子网掩码
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
subnet
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1

## Slide 41: Subnets
how many?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.1
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
Notes: 6个，除了三个子网以外，还有链接路由器的链路， ***.1.***, ***.2.***, ***.3.***, ***.7.***, ***.8.***, ***.9.***

## Slide 42: IP addressing: CIDR 无类别域间路由选择
CIDR: Classless InterDomain Routing
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 43: 子网分类，A,B,C
8位的子网地址， A类网络
能容纳多少台主机？
16位子网地址，B类网络
能容纳多少台主机？
24位子网地址，C网络？
能容纳多少台主机？

## Slide 44: IP addresses: how to get one?
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play” （即插即用协议）

## Slide 45: DHCP: Dynamic Host Configuration Protocol
goal: allow host to dynamically obtain its IP address from network server when it joins network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/“on”)
  support for mobile users who want to join network (more shortly)
DHCP overview:
  host broadcasts “DHCP discover” msg [optional]
  DHCP server responds with “DHCP offer” msg [optional]
  host requests IP address: “DHCP request” msg
  DHCP server sends address: “DHCP ack” msg

## Slide 46: DHCP client-server scenario
223.1.1.0/24
223.1.2.0/24
223.1.3.0/24
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.9
223.1.3.2
223.1.3.1
223.1.1.2
223.1.3.27
223.1.2.2
223.1.2.1
DHCP
server
arriving DHCP
client needs
address in this
network

## Slide 47: DHCP client-server scenario
DHCP server: 223.1.2.5
arriving
client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I’ll take that IP address!
Broadcast: OK. You’ve got that IP address!

## Slide 48: DHCP: more than IP addresses
DHCP can return more than just allocated IP address on subnet:
  address of first-hop router for client （网关）
  name and IP address of DNS sever
  network mask (indicating network versus host portion of address)

## Slide 49: DHCP: example
connecting laptop needs its IP address, addr of first-hop router, addr of DNS server: use DHCP
router with DHCP
server built into
router
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.1 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP
168.1.1.1
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP

## Slide 50: DHCP: example
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
encapsulation of DHCP server, frame forwarded to client, demuxing up to DHCP at client
router with DHCP
server built into
router
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
client now knows its IP address, name and IP address of DSN server, IP address of its first-hop router

## Slide 51: DHCP: Wireshark output (home LAN)
Message type: Boot Reply (2)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 192.168.1.101 (192.168.1.101)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 192.168.1.1 (192.168.1.1)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP ACK
Option: (t=54,l=4) Server Identifier = 192.168.1.1
Option: (t=1,l=4) Subnet Mask = 255.255.255.0
Option: (t=3,l=4) Router = 192.168.1.1
Option: (6) Domain Name Server
Length: 12; Value: 445747E2445749F244574092;
IP Address: 68.87.71.226;
IP Address: 68.87.73.242;
IP Address: 68.87.64.146
Option: (t=15,l=20) Domain Name = "hsd1.ma.comcast.net."
reply
Message type: Boot Request (1)
Hardware type: Ethernet
Hardware address length: 6
Hops: 0
Transaction ID: 0x6b3a11b7
Seconds elapsed: 0
Bootp flags: 0x0000 (Unicast)
Client IP address: 0.0.0.0 (0.0.0.0)
Your (client) IP address: 0.0.0.0 (0.0.0.0)
Next server IP address: 0.0.0.0 (0.0.0.0)
Relay agent IP address: 0.0.0.0 (0.0.0.0)
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Server host name not given
Boot file name not given
Magic cookie: (OK)
Option: (t=53,l=1) DHCP Message Type = DHCP Request
Option: (61) Client identifier
Length: 7; Value: 010016D323688A;
Hardware type: Ethernet
Client MAC address: Wistron_23:68:8a (00:16:d3:23:68:8a)
Option: (t=50,l=4) Requested IP Address = 192.168.1.101
Option: (t=12,l=5) Host Name = "nomad"
Option: (55) Parameter Request List
Length: 11; Value: 010F03062C2E2F1F21F92B
1 = Subnet Mask; 15 = Domain Name
3 = Router; 6 = Domain Name Server
44 = NetBIOS over TCP/IP Name Server
……
request

## Slide 52: IP addresses: how to get one?
Q: how does network get subnet part of IP addr?
A: gets allocated portion of its provider ISP’s address space
ISP's block 11001000 00010111 00010000 00000000 200.23.16.0/20
Organization 0 11001000 00010111 00010000 00000000 200.23.16.0/23
Organization 1 11001000 00010111 00010010 00000000 200.23.18.0/23
Organization 2 11001000 00010111 00010100 00000000 200.23.20.0/23
... ….. …. ….
Organization 7 11001000 00010111 00011110 00000000 200.23.30.0/23

## Slide 53: Hierarchical addressing: route aggregation 路由聚合
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning
199.31.0.0/16”
200.23.20.0/23
Organization 2
.
.
.
.
.
.
hierarchical addressing allows efficient advertisement of routing
information:

## Slide 54: Hierarchical addressing: more specific routes
ISPs-R-Us has a more specific route to Organization 1
“Send me anything
with addresses
beginning
200.23.16.0/20”
200.23.16.0/23
200.23.18.0/23
200.23.30.0/23
Fly-By-Night-ISP
Organization 0
Organization 7
Internet
Organization 1
ISPs-R-Us
“Send me anything
with addresses
beginning 199.31.0.0/16
or 200.23.18.0/23”
200.23.20.0/23
Organization 2
.
.
.
.
.
.

## Slide 55: IP addressing: the last word...
Q: how does an ISP get block of addresses?
A: ICANN: Internet Corporation for Assigned
Names and Numbers http://www.icann.org/
  allocates addresses
  manages DNS
  assigns domain names, resolves disputes
  ICANN：互联网名称与数字地址分配机构

## Slide 56: NAT: network address translation 网络地址转换
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
138.76.29.7
local network
(e.g., home network)
10.0.0/24
rest of
Internet
datagrams with source or
destination in this network
have 10.0.0/24 address for
source, destination (as usual)
all datagrams leaving local
network have same single source NAT IP address: 138.76.29.7,different source port numbers

## Slide 57: NAT: network address translation
motivation: local network uses just one IP address as far as outside world is concerned:
  range of addresses not needed from ISP: just one IP address for all devices
  can change addresses of devices in local network without notifying outside world
  can change ISP without changing addresses of devices in local network
  devices inside local net not explicitly addressable, visible by outside world (a security plus)

## Slide 58: NAT: network address translation
implementation: NAT router must:
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
    . . . remote clients/servers will respond using (NAT IP address, new port #) as destination addr
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in dest fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 59: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1
sends datagram to
128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router
changes datagram
source addr from
10.0.0.1, 3345 to
138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives
dest. address:
138.76.29.7, 5001
4: NAT router
changes datagram
dest addr from
138.76.29.7, 5001 to 10.0.0.1, 3345
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 60: NAT: network address translation
16-bit port-number field:
  60,000 simultaneous connections with a single LAN-side address!
NAT is controversial:
  routers should only process up to layer 3
  address shortage should be solved by IPv6
  violates end-to-end argument
    NAT possibility must be taken into account by app designers, e.g., P2P applications
  NAT traversal: what if client wants to connect to server behind NAT?

## Slide 61
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 62: IPv6: motivation
initial motivation: 32-bit address space soon to be completely allocated.
additional motivation:
  header format helps speed processing/forwarding
  header changes to facilitate QoS
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 63: IPv6 datagram format
priority: identify priority among datagrams in flow
flow Label: identify datagrams in same “flow.”
(concept of“flow” not well defined).
next header: identify upper layer protocol for data
交付给TCP，UDP
data
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
Notes: 流类别，长度为8bit，它等同于IPv4报头中的TOS字段，表示IPv6数据报文的类或优先级，主要应用于QoS。 Flow Label：流标签，长度为20bit，它用于区分实时流量。流可以理解为特定应用或进程的来自某一源地址发往一个或多个目的地址的连续单播、组播或任播报文。IPv6中的流标签字段、源地址字段和目的地址字段一起为特定数据流指定了网络中的转发路径。这样，报文在IP网络中传输时会保持原有的顺序，提高了处理效率。随着三网合一的发展趋势，IP网络不仅要求能够传输传统的数据报文，还需要能够传输语音、视频等报文。这种情况下，流标签字段的作用就显得更加重要。

## Slide 64: Other changes from IPv4
checksum: removed entirely to reduce processing time at each hop
options: allowed, but outside of header, indicated by “Next Header” field
ICMPv6: new version of ICMP
  additional message types, e.g. “Packet Too Big”
  multicast group management functions

## Slide 65: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields

## Slide 66: Tunneling
physical view:
IPv4
IPv4
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6

## Slide 67: Tunneling （建隧道）
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
A
B
IPv6
IPv6
E
IPv6
IPv6
F
C
D
logical view:
IPv4 tunnel
connecting IPv6 routers
E
IPv6
IPv6
F
A
B
IPv6
IPv6
IPv4
IPv4

## Slide 68: IPv6: adoption
Google（2015）: 8% of clients access services via IPv6
NIST（2015）: 1/3 of all US government domains are IPv6 capable
Long (long!) time for deployment, use
  20 years and counting!
  think of application-level changes in last 20 years: WWW, Facebook, streaming media, Skype, …
  Why?

## Slide 69
4.1 Overview of Network layer
  data plane
  control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  network address translation
  IPv6
4.4 Generalized Forward and SDN
  match
  action
  OpenFlow examples of match-plus-action in action
Chapter 4: outline

## Slide 70
Generalized Forwarding and SDN
通用转发和SDN
2
3
0100 1101
values in arriving
packet’s header
logically-centralized routing controller
1
control plane
data plane
Each router contains a flow table that is computed and distributed by a logically centralized routing controller
local flow table
headers counters actions
远程控制器
分组交换机
流表（首部，计数器，动作）

## Slide 71: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate overlapping patterns
  Counters: #bytes and #packets
Flow table in a router (computed and distributed by controller) define router’s match+action rules

## Slide 72: OpenFlow data plane abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  Pattern: match values in packet header fields
  Actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  Priority: disambiguate（消除歧义） overlapping patterns
  Counters: #bytes and #packets
src=1.2.*.*, dest=3.4.5.*  drop
src = *.*.*.*, dest=3.4.*.*  forward(2)
3. src=10.1.2.3, dest=*.*.*.*  send to controller
* : wildcard（通配符）

## Slide 73: OpenFlow: Flow Table Entries
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Rule
Action
Stats
Forward packet to port(s)
Encapsulate and forward to controller
Drop packet
Send to normal processing pipeline
Modify Fields
Packet + byte counters
Link layer
Network layer
Transport layer
Notes: Now I’ll describe the API that tries to meet these goals.

## Slide 74
Destination-based forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
51.6.0.8
*
*
*
port6
Examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
*
*
*
*
22
drop
Firewall:
do not forward (block) all datagrams destined to TCP port 22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Forward
*
*
*
*
128.119.1.1
*
*
*
*
drop
do not forward (block) all datagrams sent by host 128.119.1.1

## Slide 75
Destination-based layer 2 (switch) forwarding:
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
sport
TCP
dport
Action
*
*
*
*
*
*
*
*
port3
Examples
layer 2 frames from MAC address 22:A7:23:11:E1:02 should be forwarded to output port 6
22:A7:23:
11:E1:02

## Slide 76: OpenFlow abstraction
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood 转发或者泛洪
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port
match+action: unifies different kinds of devices
Notes: 语重心长

## Slide 77: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Example: datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 78
Chapter 4: done!
Question: how do forwarding tables (destination-based forwarding) or flow tables (generalized forwarding) computed?
Answer: by the control plane (next chapter)
4.1 Overview of Network layer: data plane and control plane
4.2 What’s inside a router
4.3 IP: Internet Protocol
  datagram format
  fragmentation
  IPv4 addressing
  NAT
  IPv6
4.4 Generalized Forward and SDN
  match plus action
  OpenFlow example

## Slide 79: 第四章课后作业
P6，P8, P11, P15, P17, P19, P20